## Slide 1: The Ocean Sound monitoring Sub-system
Giorgio Riccobene, Simone Sanfilippo and Salvatore Viola
on behalf of the LNS-INFN marine acoustics group
INFN – Laboratori Nazionali del Sud
sanfilippo@lns.infn.it

## Slide 2
Why is sound an important variable for observing the ocean at a global scale?
Ocean Sound carries information on several sources and processes in the ocean:
Climate Change: wind, waves, rain; sound propagation; ice-cap status
Ocean Health: anthropogenic acoustic pollution, monitoring of soniferous species
Safety, security: geophysical events (tsunamis earthquakes,..), illegal/banned activities, disasters,..
Attempts at international scale:
https://repository.oceanbestpractices.org/handle/11329/2405
https://oceanexpert.org/downloadFile/45461

## Slide 3
Integrate Ocean Sound in the IIOOS
(Italian Integrated Ocean Observing System)
Implementation
Data collection
(raw data inhomogeneity):
Sensor type, depth, location, sensor calibration, sampling frequency, duration of acquisition, duration of experiment, time sampling,...
Data Sharing/Exposure
Harmonise IR data sharing resources
Avoid sharing of strategic/sensible data
Data Analysis:
Definition of physical quantity, common/shared algorithms
Data FAIRness
Metadata defintion for raw and analised data
Algorithms and codes for analysis should be shared over a project code sharing platform

## Slide 4
Integrate Ocean Sound in the IIOOS
(Italian Integrated Ocean Observing System)
Harmonise data harvesting strategy:
Record not less than 5 continuous minutes of data every hour during the experiment
Use calibrated sensors (uncalibrated sensors should be used for a limited subset of analyses)
Definition of physical quantity to be derived from raw data
Sound Pressure Level (to start with)
Path for data analysis
Spectral analysis in octave thirds comprising 63 and 125 Hz (EU MSFD).
When possible supplemented with higher ones.
Spectral resolution of 1Hz should be provided for fmax<1 kHz
Spectral resolution of 100 Hz should be provided for fmax>1 kHz
Average and median values of SPL should be calculated together with the 25th, 50th, 75th and 95th percentiles
Implementation

## Slide 5: ITINERIS WP5.7 @ INFN – LNS
INFN – LNS provides:
  Python algorithms for data analysis (available on Git with permissions)
  Best practices to ensure FAIR data use
Analysis chain:
  Save 5 minutes acoustic data every 5 min (60 GB/day)
  (Real time or delayed mode) data analysis
    Produce Spectrograms
    Calculates Sound Pressure Level (dB re 1μPa) in 1/3-octave frequencies bands
      Mean, 25th, 50th, 75th and 95th percentiles
    Save outputs in PNG and HDF5 formats including metadata
      Fill an ERDDAP server (https://erddap.lns.infn.it/erddap)
    Produce WAV and MP3 files for outreach purposes

## Slide 6: ITINERIS WP5.7 @ INFN – LNS Ocean Sound monitoring Sub-system flow chart

## Slide 7: ITINERIS WP5.7 @ INFN – LNS Data analysis: SPL calculation
def spl_spec(nfft, fs, f, t, psd_spect, Freq_valid, SPLlim=0, plot=0):
# SPL calculation
# Calculation of central frequencies in octave band:
octave = 1/3
fcs = FreqBandsCalculation(octave, fs=fs)
nominal_frequencies = [16, 20, 25, 31.5, 40, 50, 63, 80, 100, 125, 160, 200, 250, 315, 400, 500, 630, 800, 1000,\
1250, 1600, 2000, 2500, 3150, 4000, 5000, 6300, 8000, 10000, 12500, 16000,\
20000, 25000, 31500, 40000, 50000, 63000, 80000, 100000]
yticks_str = []
spl_mean = np.ones([len(fcs),len(t)])*np.nan
for j in range(0,len(fcs)):
fc = fcs[j]
if fc>0:
fmax = fs/2
else:
fmax = max(fc)
flow,fup = FreqBandLimits(fc, octave)
if flow>=Freq_valid and fup<=fmax:
indx_flow = (np.abs(f - flow)).argmin()
indx_fup = (np.abs(f - fup)).argmin()
psd = psd_spect[indx_flow:indx_fup,:] #[dB re A^2/Hz]
spl = 10*np.log10(np.sum(10**(psd/10) * (fs/nfft), axis=0)) #[dB re A]
# SPL in each octave band:
spl_mean[j,:] = spl
# Removing nan values:
fcs = fcs[~np.isnan(spl_mean[:,0])]
spl_mean = spl_mean[~np.isnan(spl_mean[:,0]),:]
y = np.arange(len(fcs)+1) - 0.5
yticks=[str(int(f//1)) for f in fcs]
yyy = [int(value) for value in yticks]
for ii in yyy:
diff = min(nominal_frequencies, key=lambda x: abs(x - ii))
yticks_str.append(str(diff))

## Slide 8: ITINERIS WP5.7 @ INFN – LNS Comparison with PAMGuide
PAMGuide is an open source code (https://sourceforge.net/projects/pamguide/), written in Matlab and in R, based on the work of Merchant et al. (https://doi.org/10.1111/2041-210X.12330) widely used in the field of bioacoustics. Among the other features, it provides calculations of PSD and SPL in 1/3-octave frequency bands
In the framework of ITINERIS and the IT-OS sub-system, INFN - LNS is developing a similar code in python for the calculation of SPL in 1/3-octave frequency bands (https://doi.org/10.3390/jmse13030454) in order to standardise the analysis methodology among the ITINERIS community
Test case: PAMGuide and INFN are using the same approach to calculate PSD and SPL?

## Slide 9: ERDDAP: Metadata vocabulary
{
"Sensor":{
"Number of sensors": 1,
"Nickname": "JB4",
"Sensor ID": 164,
"Manufacturer Name": "co.l.mar.",
"Manufacturer Info": "https://www.colmaritalia.it/it/home/",
"Part number or model": "DG1330 HP",
"Serial number": "SN164",
"Sensor LF cutoff": "N.D.",
"Sensor HF cutoff": [700,"[Hz]"],
"Sensitivity":{
"Average value": [-156,"[dB re V/1uPa]"],
"Curve": "N.D."
}
},
"Mooring":{
"Mooring name": "JB4",
"Mooring type": "CABLED",
"Seabed depth": [3455,"[m]"],
"Sensor depth": [3452.4,"[m]"],
"Easting": [587733.30,"[m]"],
"Northing": [4016810.84,"[m]"],
"WGS84 Zone": "33N",
"Date of installation": "October 2024",
"Date of recovery": "N.D."
}
All the output files contain metadata
information to ensure FAIR(ness):
https://erddap.lns.infn.it/erddap

## Slide 10: ERDDAP: Datasets
https://erddap.lns.infn.it/erddap
SPL at 63 Hz

## Slide 11: ITINERIS WP5.7: INFN – LNS site nodes
Portopalo di Capo Passero (3450 m)
IPANEMA - Catania (2061 m)
IPANEMA - Panarea (24 m)

## Slide 12: Ocean Sound monitoring sub-system: Research Infrastructures
Consiglio Nazionale delle Ricerche - Istituto di Scienze Polari (CNR - ISP), Messina
Consiglio Nazionale delle Ricerche - Istituto per lo studio degli impatti Antropici e Sostenibilità in ambiente marino (CNR - IAS), Capo Granitola (Trapani)
Consiglio Nazionale delle Ricerche - Istituto di Scienze MARine (CNR - ISMAR), Venice Laguna
Istituto Nazionale di Fisica Nucleare - Laboratori Nazionali del Sud (INFN - LNS), Catania
Istituto Nazionale di Geofisica e Vulcanologia (INGV), Catania
European Multidisciplinary Seafloor and water column Observatory - European Research Infrastructure Consortium (EMSO - ERIC), Catania

## Slide 13: Conclusions and outlook
INFN - Laboratori Nazionali del Sud is leading the WP 5.7 of ITINERIS:
  Main goal is the development of the Italian Ocean Sound monitoring Sub-system
    We are efficiently storing, collecting and analyzing acoustic data from different moorings and involved RIs
    Preliminary results are compatible with standard algorithm constantly used in the field (PAMGuide)
  Acoustic data from all the INFN - LNS moorings are constantly feeding an ERDDAP server (https://erddap.lns.infn.it/erddap)
  Future steps are the finalization of the system (by including also data from a Distributed Acoustic Sensor (DAS) system) that will demonstrate one of the most innovative scientific infrastructures for the continuous monitoring of the Mediterranean Sea soundscape.

## Slide 15: ITINERIS WP5.7 @ INFN – LNS Preliminary results
Earthquake (Mwp 5.8) recorded by hydrophones at Portopalo di Capo Passero facility on 13rd May 2025 coming from a seismic event in Crete (Greece) at 22:51:16 UTC (about 1000 km away from south Sicily)
  The P-wave arrives about 200 seconds after the event
  The S-wave arrivers about 300 seconds after the event
It lasts for about 350 seconds
300
350
400
450
500
550
600
650
700
750
800
850
900
Time [s]
https://terremoti.ingv.it/event/42706112

## Slide 16: ITINERIS WP5.7 @ INFN – LNS: status update
    Ocean Sound monitoring Sub-system within the ITINERIS Data Portal:
    Python algorithms for data analysis (available on Git with permissions)
      Best practices to ensure FAIR data use
      Sound Pressure Level metrics (mean, 25th, 50th, 75th, 95th percentiles in third-octave bands)
    Metadata and vocabulary aligned with, and extending, SeaDataNet standards
    Collaboration with all involved RIs
      Two-day training with CNR – IAS at INFN - LNS
      Regular updates via remote connections
    ERDDAP server development and maintenance:
    Data samples from INFN – LNS marine nodes available through ERDDAP (including new DAS recordings from Catania and Capo Passero)
      Available at https://erddap.lns.infn.it/erddap