## Slide 1
Integrating modelling and data analysis to understand and quantify the FLASH effect
Camilla Scapicchio, Igor Bodrenko, Lorenzo Castelli, Emanuele Scifoni, Alessandra Retico, Valentina Tozzini,
PI: Leonida Gizzi

## Slide 2
UHDR, FLASH and minibeams
Ultra-high dose rate pulsed irradiation and/or spatial comb shaping of the beam
produce a selective sparing of normal tissues! (“FLASH” and “minibeam” effect )
tumor control
therapeutic window
Delivered dose (D)
normal tissue complication
Expansion of the therapeutic window
Modifying factor
Fcancer~1, Fhealthy<1
Cure & Spare
tissue, cell condition/state…
Treatment planning
~10-20 parameters
An insight into hypothesized biological mechanisms contributing to the Flash effect F Del Debbio, et al FF (2023)
Dedicated linac
Radiotherapy, kills tumor cells with ionizing radiation
Also damages normal tissues, and restricts radiotherapists actions to a narrow therapeutic window

## Slide 3
D
Expansion of the therapeutic window
Treatment planning
An insight into hypothesized biological mechanisms contributing to the Flash effect F Del Debbio, et al FF (2023)
Ultra High Dose Rate
+ time/space hyper fractioning
  ⇒ spare normal tissue
  ⇒ same or enhanced effect on tumor
  ⇒ Intrinsic selectivity at the cell level
But
F as a function of the irradiation parameters and tissue/tumor type must be known in order to get to clinical translation
UHDR, FLASH and minibeams

## Slide 4
Machine learning
minimalist empirical model
Irradiation pars
tissue data/effect
data
multi-scale simulations
paras
params
data
Treatment planning
radiobiological mechanism
Data elaboration and
analysis
The grand scheme

## Slide 5
A computational task force
Valentina Tozzini
multi-scale biomodeling
In silico Radiobiological Modeling @NANO
Igor Bodrenko
empirical models
Margherita Bini
coarse grained
models
Lorenzo Castelli
Emanuele Scifoni
Reaction-diffusion Monte Carlo
Alessandra Retico
Camilla Scapicchio
Susanna Monti
Reactive dynamics
Data organization
machine learning
F Di Martino
F Cella Zanacchi
E Da Pozzo
M Maffei
E Ciarrocchi
M Costa…
Experiments

## Slide 6
Treatment planning
Neural Network
“Brute force”
A platform for data collection/elaboration
Collect a complete set of data on the UHDR irradiation effects
Build a platform equipped with analysis and elaboration tools to train a neural network to evaluate F(P)
Issues
The training requires a large amounts of data, pre-elaborated for homogeneity
The NN gives answers with no explanation of the mechanism → unexplainability
            This might not be entirely satisfactory especially considered the medical application
machine learning
In progress

## Slide 7
Differential cell survival/
tissue sparing
fs
ps
ns
μs
ms
sec
hours
nm
μm
mm
Physical stage
Irradiation
excitation
Chemical stage
Complex radicals
Formation and diffusion
Reactions with DNA
Bio-chemical stage (intra-cell)
DNA breaks
Intra-cell signaling and diffusion
Repair/apoptosis
Tissue Level
Inter-cell signaling and
diffusion of repairing enzimes/radicals
Cell reorganization
Heterogeneous chemistry
Water radiolysis
Radicals formation and diffusion
The final effect occurs here
A completely opposite view: Direct simulation of the effect
Irradiation acts here
Mini/microbeam irradiation
UHDR+pulsed irradiation

## Slide 8
fs
ps
ns
μs
ms
sec
hours
nm
μm
mm
Physical stage
Irradiation
excitation
Chemical stage
Complex radicals
Formation and diffusion
Reactions with DNA
Bio-chemical stage (intra-cell)
DNA breaks
Intra-cell signaling and diffusion
Repair/apoptosis
Tissue Level
Inter-cell signaling and
diffusion of repairing enzimes/radicals
Cell reorganization
Heterogeneous chemistry
Water radiolysis
Radicals formation and diffusion
The radiobological effects span 15-20 order of magnitude in time and space
Possible determinants of differential effects
Oxygen concentration
⇒ Different production of ROO*
ROO* differential diffusivity
⇒ Reach different saturation level
Oxygen concentration
ROO* diffusion/saturation
reparation enzymes & related subst
Cell signaling/death/survival
Non-linear (e.g. inter-track) effects
⇒ differently activated/regulated by different architecture of cell/tissue
Activation and diffusion of
reparatory enzymes/mols
⇒ Different efficiency of DNA damage reparation
Activation of inter-cell signaling
⇒ Different damg propagation/remediation
→ survival/death
A completely opposite view: Direct simulation of the effect

## Slide 9
Months/years
fs
ps
ns
μs
ms
sec
hours
nm
μm
mm
m
Reduce resolution
Time averaging
Particle models
Continuum/
grid models
Increase empiricism
Multi-Scale modeling in a nutshel: lower the cost, increase the empiricism
Spatial coarse graining
Reduce/hide degrees of freedom
Use collective variables
Coarse graining decrease the simulation cost
Time coarse graining
Increase the time step of motion integration
cut off high frequencies
Use stochastic/enhanced sampling methods, statistical averages
… but increase the empirical level of the model
Coarse graining increase the number of parameters, and the empirical level of the model
Strategy for fitting parameters (regression/ML)
Target/input data (from
exp or higher level theory)
Network, kinetic models
Multi-scale modeling
= Use different resolution/models/ representations for modeling the different stages of a process

## Slide 10
Months/years
fs
ps
ns
μs
ms
sec
hours
nm
μm
mm
m
Reduce resolution
Time averaging
Particle models
Continuum/
grid models
Network, kinetic models
Spatial coarse graining
Reduce/hide degrees of freedom
Use collective variables
Time coarse graining
Increase the time step of motion integration
cut off high frequencies
Use stochastic/enhanced sampling methods, statistical averages
Multi-Scale modeling of bio-processes
Increase empiricism
”Parameters” coarse graining
Interactions have increasing empiricism
Strategy for fitting parameters (regression/ML)
accuracy/trasferability
Target/input data

## Slide 11
Months/years
fs
ps
ns
μs
ms
sec
hours
nm
μm
mm
m
Particle models
Continuum/
grid models
Network, kinetic models
Typical workflow of multiscale bio-modeling
Expt data
System and starting Parameterization
Adnvanced fit procedures, ML
Models
(kinetic, DE, networks)
params refinement
Dynamics
simulations
Observable calculation
The multi-scale approach involves the feedback between different stages AND with experiment
Simulations and calculations return observables to compare with experiment
Experiment gives feedback to models and aid parameterization
Simulations give prediction for quantities unaccessible to experiment
Muli-metodological integration is necessary
Predictions

## Slide 12
At any level there is a certain level of empirical content
GS
-> Use ML to parameterize the FF
The atomistic and CG empirical force fields (FFs) are many-parameters functions E[pi]
The empirical content increases as the resolution decreases
The parameterization strategy is crucial
E
Force Field
distributions
Forces
energies
trajectories
simulation
Higher level atomistic theory
Expt data set:
structures,
thermo-statistics
Fit methods:
PES matching
Force matching
Regression
IBI, Inverse MC
Entropy min…
Parameters
training

## Slide 13
Computer modeling and Machine Learning
E
Force Field
distributions
Forces
energies
trajectories
simulation
Higher level theory trajectories and Forces
training
Machine Learning CG potentials
E
Force Field
distributions
trajectories
Higher level theory
Trajectories
training
Graph Neural Networks
E
Force Field
distributions
Forces
energies
trajectories
simulation
Higher level atomistic theory
Expt data set:
structures,
thermo-statistics
Fit methods:
PES matching
Force matching
Regression
IBI, Inverse MC
Entropy min…
Parameters
training
-> Use ML to calculate forces
-> Use ML to parameterize the FF
-> Use ML to produce trajectories
Empirical potential fit
Faster simulation
Larger data amount needed for learning
Smaller explainability

## Slide 14
fs
ps
ns
μs
ms
sec
hours
nm
μm
mm
Physical stage
Irradiation
excitation
Chemical stage
Complex radicals
Formation and diffusion
Reactions with DNA
Bio-chemical stage (intra-cell)
DNA breaks
Intra-cell signaling and diffusion
Repair/apoptosis
Tissue Level
Inter-cell signaling and
diffusion of repairing enzimes/radicals
Cell reorganization
Heterogeneous chemistry
Water radiolysis
Radicals formation and diffusion
Possible determinants of differential effects
Oxygen concentration
⇒ Different production of ROO*
ROO* differential diffusivity
⇒ Reach different saturation level
Oxygen concentration
ROO* diffusion/saturation
reparation enzymes & related subst
Cell signaling/death/survival
Non-linear (e.g. inter-track) effects
⇒ differently activated/regulated by different architecture of cell/tissue
Activation and diffusion of
reparatory enzymes/mols
⇒ Different efficiency of DNA damage abnd reparation
Activation of inter-cell signaling
⇒ Different damg propagation/remediation
→ survival/death
Getting back to our problem, we are currently focusing on two scales

## Slide 15
Radicals evolution scheme
fs
ps
ns
μs
ms
sec
hours
nm
μm
mm
The mechanism is regulated by
Oxygen concentration
Several feedbacks on radicals and oxygen concentration
Highly non linear!
The mechanism generates
DNA damage
Oxidative stress
Multiple damage pathways, different time scales

## Slide 16
fs
ps
ns
μs
ms
sec
hours
nm
μm
mm
Current hypotheses
ODH is qualitatively correct but quantitatively insufficient
Oxygen has certainly a role however with feedbacks at several different levels: High non linearity
Other mechanisms at different time scales
Radicals evolution scheme –the role of oxygen
Wilson J. Et al. (2020) Front. Oncol redrawn from Pratx et al.2019
Oxygen is consumed to generate radicals, and this generate transient hypoxia, which induce radio-resistance
At High dose rate: Oxygen consuption is too quick to be within the pulse period which prolongs radio-resistance
Effect smalle in cancer cell because already hypoxic
(Already suggested in Hall&Brenner 1991)
Zhou Med Phys 2020
Oxygen depletion hopothesis:
a traditional explanation
The effect would depend on a fine balance between the oxygen restoration time and the irradiation dynamics
The dependence of the oxygen dynamics on the cell type/environment/state is unclear

## Slide 17
fs
ps
ns
μs
ms
sec
hours
nm
μm
mm
The atomistic scale:
Combining reaction-diffusion monte carlo with reactive MD
Simulate the water radiolysis, formation/diffusion of radicals and reaction with DNA
Probing Spatiotemporal Effects of Intertrack Recombination with a New Implementation of Simultaneous Multiple Tracks in TRAX-CHEML Castelli, G Camazzola, MC Fuss, D Boscolo, M Krämer, V Tozzini, E scifoni IJMS 26 (2), 571 (2025)
Indirect DNA damage by hydroxyl radicals: a molecular dynamics assessment L Castelli, E Scifoni, V Tozzini Phys Med (2026)

## Slide 18
fs
ps
ns
μs
ms
sec
hours
nm
μm
mm
Computer simulation of water radiolysis and formation early evolution/diffusion of ROS and interaction with biomolecules
Time-size scales: up to μsec and μm
Method: combine two “complementary” approaches
Reaction-diffusion Monte Carlo
Reactive atomistic molecular dynamics
Starting from the beginning… First steps of ROS generation

## Slide 19
nm
μm
mm
MC
MD
Combining Monte Carlo & Molecular dynamics
Simulation procedure: Probability driven (Metropolis, MC) track based
Input: Cross sections, kinetic constants & diffusion coefficients; radiation type, energy and quality
Time/space scales: fs to μs, nm to μm
Output: tracks and spatial distribution in time of chemical species
fs
ps
ns
μs
ms
sec
hours
Reaction-diffusion Monte Carlo
Reactive atomistic molecular dynamics
(RDMC)
Boscolo, Scifoni et al 2018-2024
Castelli, Petrolli, Micheloni 2020-2024

## Slide 20
nm
μm
mm
MC
MD
Combining Monte Carlo & Molecular dynamics
fs
ps
ns
μs
ms
sec
hours
Reactive atomistic molecular dynamics
Starting space distribution of species
(RAMD)
Integration procedure: reactive MD FFs force driven trajectory based
Input: Interactions box of water molecules,
+ other molecules of interest in starting state
Time/space scales: fs to μs, nm to μm
Output: Trajectories of each particle, reactions evolution and diffusion, kinetic constants for new species (e.g. DNA)
Kinetic
constants
Diffusion coefficients
MC and MD are complementary!

## Slide 21
MC and MD are complementary!
MC
MD
PROS
CONS
Less computationally expensive
Same method can easily include different radiation type and quality
Can follow evolution of species on long time and large distance scales
Larger scales capability
More computationally expensive
Need starting distribution of species and their energy
Needs a starting effort to parameterize interactions
Needs coarse graining to go on the long/large scales
Larger computational cost
Gives the evolution trajectories of all particles of the system in time
Diffusion coefficients, cross sections etc, reaction probabilities… are not needed, output of simulations
Different molecules of any type can be added with no additional effort
Larger predictive power
Many parameters are needed: diffusion coefficients, cross sections … for all species and processes included in the calculations
Including different species and/or environmental conditions requires additional parameters
Larger empirical level

## Slide 22
DNA, proteins,
other molecules
Trajectories
Tracks
MC and MD are complementary!
Radiation properties
Cross sections
Diffusion coefficients
(water and its ions/radicals)
OH*
MC
Water box + radicals/ions distributions
MD
+Cross sections
Diff coefficient etc of complex radicals and DNA
DNA damage

## Slide 23
Interfacing MC with MD provides a complete view
Reactive MD simulation of radicals formation and diffusion and interaction with DNA are in the course, which will disclose the dependence of DNA damage on different radicals concentration and the damage mechanisms
Δx
Δt
Preliminary results on MC indicate strong non linear effects on [O] and [R*] due to space-time vicinity of radiation tracks
→ UHDR effects
Lorenzo Castelli PhD thesis

## Slide 24
fs
ps
ns
μs
ms
sec
hours
The coarse grained scale:
DNA damage evolution and beyond
The super-resolution data show DNA damaging in clusters and sub-clusters on the 100-300 nm scale, whose structure depends on the CONV/FLASH irradiation modality (data from F Cella group)
Coarse Grained model at the nucleosome level…
Simulate:
Chromatin in different compaction states
Different level of damage
Dynamics of chromatin after damage
…
In progress
Editorial: Multidisciplinary approaches to the FLASH radiotherapyF Di Martino, E Scifoni, V Patera, P Montay-Gruel, F Romano, A Arafhshesh, V Tozzini Frontiers in Physics 12, 1439081 (2025)

## Slide 25
Between direct modeling and AI brute force: empirical models
Machine learning
minimalist empirical model
Irradiation pars
tissue data/effect
data
multi-scale simulations
paras
paras
data
Treatment planning
radiobiological mechanism
Data elaboration and
analysis

## Slide 26
Cell deadly damage
critical sites are damaged
α=2
α=4
α=3
β=0.8
Biological
damage
Ionization and production of radicals
dose released by a track
threshold for local damage
Direct damage
α=4
α=3
α=2
α=1
Indirect local damage
threshold for cell damage β
Pulsed irradiation + recombination/repair
time
tr
tp
R
Pulsed irradiation
Intrapulse Diffusion Recombination Interpulse Repair biological effects
fsec nsec μsec msec sec min
radicals diffusion
beam fractioning
Micro/Minibeam
A minimalistic stochastic model
The model includes
Stochasticity
Multiple level thresholds
Diffusivity
Cell structural features
Recombination/repair
Minimal number of parameters
The model returns
FLASH effects due to diffusion
(No UHDR for direct damage)
Minibeam effect
Dose modifying factor
Mc sensitive loci
2Rt

## Slide 27
We built a model with the following Features: (I Bodrenko)
Minimal number of empirical parameters accounting for the behavior of F
Essential structural features (e.g. sensitive nucleous loci)
Essential non linear effects (threshoulds on damage, stochasticity)
Intra-cell diffusivity and non homogeneous ionization
Preliminary results
The combination of mesoscopic flucutations, stochastic damage and diffusivity imply the dependence of damage probability on dose rate, i.e. the UHDR effect
Adding a threshould on multiple sites damage, one also obtain a threshould on the dose triggering FLASH effect
The model is being extended to include pulsed radiation and space distribution (also from MC simulations)
The model has a limited number of parameters related to physical quantities and can easily include experimental or MC data
These can be either fixed, fitted or optimized with ML algorithms while preserving explainability
It can be readily adapted to the treatment planning system
I Bodrenko, V Tozzini, in preparation
A minimalistic stochastic model

## Slide 28
Summary and conclusions
Milestone M 1.2 aggregated M 1.2.1-M 1.2.3
Design of the in silico multi-scale procedure and preliminary setup
Radiobiological effect simulations, and quantification of the radiation parameters-effect relationship
Database setup and implementation
Specific Results
Database and platform currently up and in population phase
Monte Carlo+Reactive dynamics atomistic simulations performed
Coarse grained models built for chromatin simulation
Minimalistic Model for calculation of dose modifying factor built preliminary result returned
Machine learning
minimalist empirical model
data
multi-scale simulations
paras
paras
data
Data elaboration and
analysis

## Slide 29
Summary and conclusions
Perspectives: further steps to clinical translation
Continue database population and establish as general standard for data
Enrich the platform with analysis tools
Use data to learn predictive NN for the effects
Machine learning
minimalist empirical model
data
multi-scale simulations
paras
paras
data
Data elaboration and
analysis
Use coarse grained models to follow the evolution of intra-cell DNA damage
Integrate the coarse grained model with atomistic simulations to elucidate molecular mechanisms
Optimize the minimalist model for different tissue and cancer type to predict the dose modifying factor

## Slide 30
Summary and conclusions
Acknowledgements
Giulia Asero, Maria Giuseppina Bisogni, Paolo Bosco, Simone Capaccioli, Satia Caroti, Andrea Cavalieri, Mariagrazia Celentano, Francesca Cella Zanacchi, Esther Ciarrocchi, Mirko Corosu, Mario Costa, Eleonora Da Pozzo, Francesca Del Debbio, Elisa De Santis, Beatrice Di Marco, Fabio Di Martino, Giulia Furini, Ruben Gianeri, Francesco Laruina, Simone Lossano, Margherita Maffei, Enrico Mazzoni, Eduarda Mota Da Silva, Piernicola Oliva, Vinoshene Pillai, Filippo Rossi, Gaia Scabia, Valeria Sipala, Enrica Strettoi