## Slide 1: Correlation Study of Integrating Current Transformer Charge and Lanex Screen Emission Signal in High-Energy Beam Measurements
D. Gregocki, F. Avella, F.Baffigi, G. Bandini, G. Benincasa, F. Brandi, M. Ezzat, A. Fregosi, L. Fulgentini, P. Koester, L. Labate, D. Palla, M. C. V. Panaino, S. Piccinini, M. Salvadori, S. G. Vlachos & L. A. Gizzi.
Milestones 1.1 and 1.6
Cascade grant LPA-STAR

## Slide 2
Table of contents:
01 - Motivation
Why integrating current transformers are usefull
02 - General description
Operating principle and signal processing
03 – Experimental setup
Measuremetns performed at ILIL, CNR-INO
04 - Results

## Slide 3: 01 -Motivation
Integrating current transformers (ICT) have been used as reliable charge diagnostics in the radio-frequency acceleration’s community
Quickly gained popularity also in laser-plasma acceleration (LPA) field thanks to nondestructive, energy independent (and compact) charge measurement
  However, in some cases
    ICT measurements overestimated charge by more than an order of magnitude1.
    ICT measurements overestimated charge by 3-4 times2.
    Charge measurement consistent with calibration – Measurement at large distance (4m) from interaction region3.
  Main unwanted contributor to charge overestimation was electro-magnetic pulse (EMP) signal
    Can we correlate ICT charge and Lanex screen emission signal?
    Is EMP influence observed also in our case?
1Glinec et al., Rev. Sci. Instrum. 77, 103301 (2006)
2B. Hidding et al., Rev. Sci. Instrum. 78, 083301 (2007)
3K. Nakamura et al., PRST-AB 14, 062801 (2011)

## Slide 4
ICT consists of a coil with magnetic core shaped into a loop through which electron bunches can pass
Electron charge induces a voltage in the coil
Integrating over this voltage produces an output voltage proportional to the electron beam charge
Integrator (part of the ICT controller) consists of op-amp, filter …
02 – General description
1
2
3

## Slide 5
One window integrates the signal, and the second one integrates the background for noise reduction
02 – General description
Ideal signal for integration
Signal from LPA generated electrons

## Slide 6
One window integrates the signal, and the second one integrates the background for noise reduction
02 – General description
Ideal signal for integration (Example)
Signal from LPA generated electrons

## Slide 7
LPA generated electrons passed through the Lanex screen after the vacuum-air transition
Afterwards they passed through ICT
Lanex emission signal was captured by CCD
03 – Experimental setup
1
2
3
4
Lanex

## Slide 8
ICT mount/shielding was designed in Blender
3D printed with PLA filament
The front part allows the main shielding to be replaced
03 – Experimental setup
Front

## Slide 9
From the linear regression:
  R2 = 0.97
  𝜒2 = 3.06
  Pearson coefficient = 0.98
Correlation between the electron charge and Lanex emission signal is present
04 – Results

## Slide 10
Summary
ICTs provide noninvasive, energy-independent charge measurements
In laser-plasma acceleration, EMP signals can influence ICT results
During the experiment, EMP signal spikes were observed
  However, correlation between the ICT charge and Lanex emission signal was still preserved
At the moment, an experiment aimed at retrieving the charge from the radiochromic films is being conducted
  To assess whether the ICT is overestimating the measured charge

## Slide 11
Experimental investigation on biomedicine
This work was supported by the PNRR MUR project ECS00000017-"Tuscany Health Ecosystem & the LPA – STAR project, funded by the European Union – Next Generation EU
Laser Development
This work was supported by the EU Horizon IFAST, under Grant Agreement No.101004730
Infrastructure Development
This work was supported by the PNRR MUR project IR0000016-I-PHOQS, funded by the European Union – Next Generation EU and EuPRAXIA Advanced Photon Sources – EuAps (IR0000030, CUP I93C21000160006).
Advanced Photon Sources
Acknowledgement

## Slide 12
Backups
Background

## Slide 13
Backups
Beam went through
Low Lanex Signal
Partial ICT hit