## Slide 1
Serena Doni
CNR IRET Conference
Rome, February 18th-19th 2025
The global production of marine bivalves is approximatively 15 million tons per year. Many of the shells are disposed of illegally
«GReen ENgineering solutions: a new LIFE for SEdiments And Shells»
S. Doni, E. Peruzzi, C. Macci, I. Rosellini, M. Di Leo, C. Vitone, M. Mali, R. Petti, G. Masciandaro
Start: 01/10/23 - End: 01/10/28
Total amount: € 3.930.225
SHELLS
CER (EWC) 020103
WASTES FROM AGRICULTURE, HORTICULTURE, AQUACULTURE, FORESTRY, HUNTING AND FISHING
In Europe the volume of potentially contaminated dredged sediments is estimated at 200 million cubic meters per year
DREDGED SEDIMENTS
CER (EWC) 170505
WASTES FROM DREDGING
ACTIVITY – SLUDGES
paving
blocks
Background
GREENLIFE4SEAS project
Dredging sediment
Stabilized
sediment
Shell powder
mass stabilization
breakwater
blocks
selected microorganisms
organic nutrients
mineral salts
catalytic oligoelements
enzymatic components
natural growth factors
Monitoring of sediment decontamination
Landfarming process
with bioactivators
Remediation of contaminated sediments
Barletta Port Bari Port
La Spezia Port Piraeus Port
PROJECT LOCATION
Bari
Barletta
Soil Texture: silty loam
OBJECTIVE
In-situ recovery and reuse of
dredged sediments and shells, as secondary raw materials for the realisation of sustainable and innovative by-products for building sector, through an optimised mixing technology
 | Bari | Barletta
pH | 8,61 | 8,89
Electrical Conductivity (dS m-1) | 55,0 | 34,9
Total Nitrogen (%) | 0,14 | 0,20
Total Organic Carbon (%) | 1,12 | 3,27
C/N ratio | 8 | 16
Total Phosphorus (mg kg-1) | 662 | 657
Cation Exchange Capacity (meq 100g-1) | 22,5 | 13,7
Petroleum hydrocarbons (C>12) (mg kg-1) | 1242 | 362
Sediment characterization
Pilot-plant
Lab-scale